O/o the Telecom.  District  Manager,

Doorsanchar  Bhawan,

Bolangir  - 767001.

Tel – (+91) 6652 - 234001, 234500 (F)

No.:W-78/2008-09/28		                                             Dtd at Bolangir 13/05/2008

# SECTION-I

# NOTICE INVIING TENDER

Sealed tenders (Packing PVC Tape/Sealing Wax) are invited for and on behalf of BHARAT SANCHAR NIGAM LIMITED by the Telecom District Manager,  Bolangir  from  the bonafide and registered contractors having experience in earthing of Tele Exchanges / WLL Station / Mobile BTS station in BSNL  ( as per the specification at page- 3)  for the earthing works in the different exchanges of Bolangir  Telecom District for the year 2008-09

| 01. | Name of work | : | Earthing work in Bolangir Telecom District. |
| --- | --- | --- | --- |
| 02. | Tentative Qty. of work | : | Enclosed |
| 03. | Tentative cost of tender | : | Rs.13,75,000/- |
| 04. | Cost of Bid document (Non refundable) | : | Rs. 520/- |
| 05. | E.M.D. | : | Rs.27,500/- |
| 06. | Mode of deposit for both Tender Paper and EMD. |  | Cash/D.D in favour of Accounts Officer (Cash), BSNL, O/o. TDM, Bolangir payable at Bolangir . |
| 07. | Tender papers can be had from | : | SDE (Est.), 1st Floor, O/o. TDM, Bolangir |
| 08. | Period of issue of Bid documents | : | All working days between 10.30 hours to 13.00 From 16.05.2008 to 29.05.2008 |
| 09. | Time and Last date of submission of bid document | : | Up to 13.00 hours of 30.05.2008 |
| 10. | Time and date of opening of bid document | : | At 16.00 Hrs of dt 30.05.2008 If the date is declared as holiday the opening date will automatically extended to next working day. |
| 11. | Criteria for issue of Tender paper | : | On production of : |
|  |  |  | A | Copy of Experience Certificate from an officer not below the rank of Dy. G.M (BSNL) or equivalent. |
|  |  |  | B | Cost of Tender paper in Cash/D.D./ drawn in favour of Accounts Officer (Cash), BSNL, O/o. TDM, Bolangir payable at Bolangir |
| 12. | Rejection of Tender | : | Unsealed, late receipt, incomplete tender, ambiguous and conditional tender will be rejected |
| 13. | Down loaded Tender form | : | Down loaded from website must contain additional D.D of Rs 520/- as cost of tender form. |

The TDM, Bolangir  reserves the right to accept or reject any or all the tenders without assigning any reason what so ever and is not bound to accept the lowest tender. For more details please visit us our website:-   www.orissa.bsnl.co.in

SPECIFICATION & SCOPE OF WORK

1.

SPECIFICATION:  The work will be carried out as per the following specification. The required diagram is also available with this tender document.

(i) Earth pit :  Normal depth of the earth pit will be 10 ft. length X 10ft. breadth X 15ft depth.

(ii) Earthing Plates to be used : 4 numbers of copper plates of size 2’ X 2’ X 4mm thickness  are to be placed on four corners of the  pit  vertically at about 1.5feet above  the bottom as shown in the diagram.( please consult diagram available inside the tender document.) Two Copper strips from two diagonally opposite   copper plates from the earth pit will be extended upto the earth bus-bar which has preferably to be inside the MDF or Switch Room and both the Bus bar and Copper strip have to be fastened with copper nuts and bolts of  proper size of copper sockets including materials  & lugging etc. Additional holes of some five to six nos has to be made on the body of the bus bar in order to extend the earth to different equipments.

(iii) 	Connections : All copper plates are to be connected with each other by copper flats/strips Tightened with copper nuts and bolts  to the  edges of all plates. Two nos of holes have to be made on both the plates and strips and it has to be tightened with copper nots and bolts of proper size, in order to have better contact of the strip with the copper plates. Similarly copper flats/strips  are  to be tightened with copper nots and bolts cross- wise as per the diagram.  . Two Copper strips from two diagonally opposite   corner copper plate inside the earth pit upto the earth bus-bar are to be extended with suitable  terminations with proper size of copper sockets including materials  & lugging etc.

The two strips coming from two copper plates  are  to be fastened with two nos. of  G.I. pipes

of  size 50mm diameter, by copper wire. The two nos  of GI pipes has to be kept  3ft apart from each other vertically and the strips will be taken out from the G.I. pipe just two feet (or as per convenient) below the earth level which will be further extended up to the Earth Bus Bar of the Exchange and terminated there. In case of new exchange where provision of Earth Bus Bar is to be made, one copper strip of size 10” X 2” X 6mm thickness with insulators and nuts, bolts of brass/copper are to be used for the purpose. Two nos of  G.I. caps are to be provided at the top of the 15ft.. G.I. pipe which will be used to pour water as and when required.

- Filling up of the pit : The  first one foot from the bottom of the earth pit  is to be filled up with  soft  soil  and then half  foot will be filled up with charcoal. Above this the four plates are to be kept vertically and they have to be interconnected as described earlier.  Then soft soil and charcoal has to be filled up in layer by layer alternately of half foot thickness up to the ground level as per the diagram  enclosed with this tender document.. The remnants (the soil coming out after digging the pit) around the earth pit is to be cleaned properly.

The earthing work should be carried out as per  BSNLstandard specified above . Before putting the earthing  materials inside the pit, the pit has to be checked for its dimension specified, and  the inter connection has to be checked as per  its standards and specification by concerned SDO/SDE or else if required by the DE(Extl) as directed by  TDM.

Payment will be made after the successful A/T of the earthing done by the contractor, if the ohmic value of the earth is 0.5 ohms or less, otherwise the payment will be held up till rectification and successful A/T is completed bringing down the earth value  ≤0.5 ohms.

- The Successful bidder has to deposit a sum of Rs.100000/-(Rupees One Lakhs ) only  as performance security deposit in shape of DD or BG  for a period of  three year from any scheduled bank at Bolangir  payable to A.O.(Cash), BSNL, O/O the TDM, Bolangir . After  completion of three  years from the date of agreement, the performance security will be refunded.

- Addressing the tender : The Sealed Envelopes containing all the required documents should be superscripted as “Tender  for carrying out Earthing  work in Bolangir  Telecom District for the year 2008-09” and  be addressed to the Divisional Engineer (P&A), BSNL, O/O TDM,Bolangir  and dropped in the tender box. available in his official chamber before the stipulated date and  time. Rate should be quoted clearly both in figures and words. However the rate quoted in words will be taken as the final rate as per rules. Any correction should be clearly scored out under proper attestation of the bidder.

- Quantum of work : Approximately 25 Nos Earthlings will be required during the year.

Details of Item and quantity of work for making earthlings at 25 sites in Bolangir  SSA

| Sl. No. | Schedule of work | Quantity | Unit |
| --- | --- | --- | --- |
| 1 | Digging of earth pit 10’ X 10’ X 15’ and boring at the two corners of the earth pit for about 10 ft or more depending on the nature of soil, if required to introduce the copper strip to obtain the ohmic value of the earth less than 0.5 ohms | 25 nos. | Per pit |
| 2 | Supplying soft soil for filling the earth pit | 750 | Per Cum |
| 3 | Supplying Charcoal for the earth pit | 375 bag | Per Bag |
| 5 | Charges for filling up the earth pit with soft soil, char coal and mixture in layer by layer alternately of half foot thickness upto the ground level as per the diagram | Per Pit | Per Pit |
| 6 | Supplying and fixing of copper plate of size 2’X2’X 4 mm in the earth pit including making holes fitting of nuts & bolts with the Copper strip. | 100 nos. | Per Plate |
| 7 | Supplying and providing G.I. pipe of medium gauge of size 15’ length of 50 mm. Dia | 25 nos. | Per pipe |
| 8 | Supplying and making earrth connections with Copper strip upto the earth bus-bar of the Exchange and making terminations with proper size of copper sockets including materialized lugging etc. | 750 Kg. | Per Kg. |
| 9 | Removal of surplus earth from the site and spreading inside the compound as per direction of BSNL official/officer | 25 | Per Site |

- Cost of Bidding : The Bidder shall bear the cost associated with the preparation and submission of the bid. BSNL, in no case will be responsible to bear these costs regardless of the conduct or outcome of the bidding process.

- Documents to be submitted along with the bid :

- EMD Rs 27,500/- in shape of DD in favour of AO (Cash), BSNL, O/O TDM, Bolangir

- Experience certificate from an officer not below the rank of Dy.G.M.(BSNL) or equivalent.

- Xerox copy of PAN CARD.

- All documents should bear the signature of the bidder/authorized person.

- Annexure-III where rates should be quoted clearly both in words and figures.

The tender will be opened in presence of the bidders or their authorized persons those who

like to be present on the scheduled date & time.

7.	SUBMISSION OF TENDER

A)	The completed tender with required documents are to be submitted in two parts. The first envelope (Packing PVC tape/sealing wax) must be marked as “Technical Bid” will contain (1)  Attested Xerox copy of PAN Card (2) Attested Xerox copy of Experience Certificate (3) EMD of Rs 27,500/- in favour of Accounts Officer (Cash), BSNL, O/o. TDM, Bolangir  in  shape of DD payable at Bolangir , (4) Tender document duly filled and signed by the bidder on each and every page with his seal, (5) Near  Relative  Certificate as per Annexure-II, (6) Any other required document like partnership deed etc. and the second envelope (Packing PVC tape/sealing wax) marked as “Financial Bid” will contain the tender quoting rates as per Annexure - III of tender document duly filled in. Financial Bid will be opened only when all documents in the first envelope (Technical Bid) are found in order. Date for opening of the Financial Bid will be notified later on after scrutiny of Technical Bid.

B)	.Mode of Dropping of Tender Paper : i)Completed Tender papers in a perfectly  sealed

envelope is to be dropped in the tender Box available in the Chamber of D.E. (P&A), O/o TDM,

Bolangir .

- EMD may be forfeited in the following case:

- If the bidder withdraws his bid during the validity period of 60 days from the date of financial bid opening.

- Production of false/fabricated documents

- If the successful bidder fails- i) to deposit the performance security within the prescribed time. ii) sign the contract within the prescribed period in the prescribed agreement form.

EMD of unsuccessful bidders will be returned as early as possible after finalization of tender but not later than 45days after expiry of bid validity without any interest.

  - Evaluation.

i)	BSNL shall evaluate the bids on the basis of overall cost in making the earth. Generally, it checks   to determine whether the tender is complete in all respect, whether any computational errors have been made, whether documents have been properly signed and whether bids are generally in order.

ii) 	If there is a discrepancy between words and figures, the amount in words shall prevail. Prior to detailed evaluation, BSNL will determine the substantial responsiveness of each bid to the document. A substantially responsive bid is one, which confirms to all the terms and condition of bid documents without material deviation. A bid determined as substantially non-responsive will be rejected by BSNL.

- Signing the contract : The successful bidder is to sign an agreement with BSNL authorities in the prescribed form on a ten-rupee non-judicial stamp paper.

- Performance Security.

- The successful bidder shall be required to deposit an amount of Rs 100000/- towards performance Security.

- Performance Security shall be submitted in the form of Bank Guarantee or A/C payee DD issued by a scheduled Bank at Bolangir .

- Performance Security will be discharged after completion of three years from the date of agreement.

- If the contractor fails or neglects any of his obligations under the contract it shall be lawful for BSNL, to forfeit either whole or any part of performance security furnished by the bidder as compensation for any loss resulting from such failure

TERMS AND CONDITIONS OF TENDER

- Execution Time Limit : The time period as stipulated in the  work order or letter of intent shall be deemed to be essence of the contract.

- Termination of Contract:

- BSNL may without prejudice to any other remedy for breach of contract may terminate the contract in whole or in parts.

(a)	If the contractor fails to execute the work within the period specified in the  work Order  or any extension thereof granted by BSNL.

(b)	If the contractor fails to perform any other obligation under the contract.

- BSNL may without prejudice, to other rights under law or the contract provided, get the work done through any other agency/party or departmentally at the risk and cost of the contractor. In the above circumstances the amount so spent will be recovered from the performance Security or any other bill of the contractor.

- Termination of Insolvency :	 BSNL may also by giving written notice and without compensation to the contractor terminate the contract if the contractor becomes unwilling, bankrupt or otherwise in any way without affecting the right of action or remedy as hirer.

- Force Majure : If any time, during the continuance of this contract, the performance in whole or in part by either party of any obligation under this contract is prevented or delayed by reason of any war or hostility, acts of the public enemy, civil commotion, sabotage, fires, floods, explosions, epidemics, quarantine restrictions, strikes, lockouts or act of God (Herein after referred to as events) provided notice of happenings, of any such eventuality is given by either party to the other within 21 days from the date of occurrence thereof, neither party shall by reasons such events be entitled to terminate this contract nor shall either party have any claim for damages against the other in respect of such on performance or delay in performance under the contract shall be resumed as soon as practicable after such an event may come to an end or cease to exit, and conclusive, provided further that if the performance in whole or part of any obligation under this contract is prevented or delayed by reason of any such event for a period exceeding 60 days either party may, at his option terminate the contract.

- Arbitration:

- In the event of any question, dispute or difference arising under the agreement or in connection there with (except as to matter the decision to which specifically provided under this agreement), the same shall be referred to sole arbitration of the TDM, Bolangir , BSNL. In case his designation is changed or his office is abolished then in such case to the sole arbitration of the officer for the time being entrusted whether in addition to the function of the TDM, Bolangir  or by whatever designation such officers may be called (herein after referred to as the said officer) and if the TDM, Bolangir  or the said officer is unable or unwilling to act as such, than to the sole arbitration of some other person appointed by the CGM/PGM/TDM or the said officer. The agreement to appoint an arbitrator will be in accordance with the Arbitration and Conciliation Act, 1996.

ii)	The arbitrator may from time to time with the consent of both the parties enlarge the time frame for making and publishing the award. Subject to aforesaid arbitration and conciliation Act, 1996 and the rules made the under, any modification thereof for the time being in force shall be deemed to apply to the arbitration proceeding under this clause.

iii)	The Venus of the arbitration proceeding shall be Office of Telecom District Manager, Telecom District, BSNL, at Bolangir  or such other place as the arbitrator may decide.

- Set Off : Any such of money due and payable to the contractor (including security deposit refundable to him) under his contract may be appropriated by BSNL and set off the same against any claim of BSNL for payment of a sum money arising out of this contract or under any other contractor with BSNL.

- Payment Terms : Payment will be made only after  clearance of A/T.. The bill should be certified by the concerned SDO and countersigned by his DET.

- 22.	Other Terms & Conditions of Tender.

(i)      TDM, Bolangir  reserves the right to accept or cancel any or all the tenders  without assigning any reason thereof.

(ii).	The successful bidder has to enter into an agreement for a period of one year from the date of agreement.

        - The period of contract should be valid for one year from the date of signing the agreement.

(iv)	TDM reserves the right to distribute  work  among the responsive contractors who are willing to work at the approved rates, if the TDM feels so to achieve the targets.

(v)	In case of any dispute the decision of the TDM, Bolangir  is final and binding.

(vi)	The TDM, Bolangir has the right to extend the contract period or quantum of work depending on the urgency of work if necessary in the interest of BSNL.

  - Warranty.  - The Tenderer has to give a warranty period of 2 (Two) years after date of commissioning. During the warranty period the earthing should be within departmental standards( < .5 ohms) ,If the earthing degrades during  warranty period, the Tenderer has to repair it on free of cost.

Telecom District Manager

O/O TDM, Bolangir .

Copy to:

  - V.O./DGM(Planning), O/O CGMT, Orissa Bhubaneswar.

  - Notice Board of this office.

  - Three wide circulated news papers.

Telecom District Manager

O/O TDM, Bolangir .

#### (Annexure-I)

#### EARTHING DIAGRAM  FOR BOLANGIR SSA

#### AGREEMENT

#### The agreement is hereby executed between Sri _____________________________________

#### S/O Sri _______________________    Vill:________________P.O.________________, P.S._______________Dist:____________as one party

#### AND

#### the Telecom District Manager Telecom District, Bolangir  on behalf of  BHARAT SANCHAR NIGAM LIMITED as the second party on this date of ……………for  carrying out the earthing work as per the specifications of tender, at the exchanges  in Bolangir  Telecom District.

#### Where as in response to the tender notice No.…………………dated………the contractor Sri, ……………………..……………………has agreed to execute the work at the approved rate through out the contract period.

Further Sri………………………………………….is declared as approved contractor for execution of Earthing work of the Telecom District Manager, Telecom District, Bolangir  for one year from the date of signing the agreement.

Sri…………………………………………..further agrees to demand the payment only after getting the earthing cleared by A/T i.e. only when the ohmic value of the earth is within 0.5 ohms. In case, the contractor fails to provide such stipulated value of earth, no payment will be made unless it is rectified.

Sri………………………………………….further agreed that the above approval can be cancelled at any time for failure on the part of the contractor to get the work executed successfully.

Signature of Contractor 					Signature of TDM

O/O TDM, Bolangir

Name								Name

Address							Address:

Signature of Witness						Signature of witness

Address							Address:

Performance Security Guarantee Bond

In consideration of the President of the India (hereinafter called “the Government”) having agreed to exempt ____________________(hereinafter called “the said contractor(s)’) from the demand under the terms and conditions of an agreement/(Purchase Order) No ______________________________________dated_____________________made Between ______________________________and_______________________(hereinafter called “the said agreement”) of security deposit for the due fulfillment by the said contractor (s) of the terms and conditions contained in the said Agreement, on production of the bank guarantee for______________________________________________________we. (name of the bank)________________________________(hereinafter refer to as “the bank”) at the request of ___________________________(contractor(s) do hereby undertake to pay to the Government an amount not exceeding_______________ against any loss of damage caused to or suffered or would be caused to or suffered by the Government by reason of any breach by the said Contractor(s) of any of the terms or conditions contained in the said Agreement.

2.	We (name of the bank) ___________________do hereby undertake to pay the amounts due and payable under this guarantee without any demure, merely on a demand from the Government stating that the amount claimed is due by way of loss or damage caused to or would be caused to or suffered by the Government by reason of breach by the said contractor(s)s failure to perform the said Agreement.  Any such demand made on the bank shall be conclusive as regards the amount due and payable by the Bank under this guarantee where the decision of the Government in these counts shall be final and binding on the bank.  However, our liability under this guarantee shall be restricted to an amount not exceeding _____________________________________________________

- We under take to pay to the Government any money so demanded notwithstanding any dispute or disputes raised by the contractor(s)/ supplier(s) in any suit or proceeding pending before any court or tribunal relating thereto our liability under this present guarantee being absolute and unequivocal, The payment so made by us under this bond shall be valid discharge of our liability for payment there under and the contractor(s)/ supplier(s) shall have no claim against us for making such payment.

- We (name of the bank)____________________ further agree that the guarantee herein contained shall remain in full force and effect during the period that would be taken for the performance of the said agreement and that it shall continue to be enforceable till all the dues of the Government under or by virtue of the said Agreement have been fully paid and its claims satisfied or discharged or till ___________________________________________(office/Department) Ministry of ________________________certifies that the terms and conditions of the said. Agreement have been fully or properly carried out by the said contractor(s) and accordingly discharges this guarantee.  Unless a demand or claim under this guarantee is made on us in writing on or before the expiry of TWO/TWO AND HALF/THREE YEARS (as specified in P.O.) from the date hereof, we shall be discharged from all liabilities under this guarantee thereafter.

- We (name of the bank)__________________________further agree with the Government that the Government shall have the fullest liberty without our consent and without affecting in any manner our obligations there under to very any of the terms and conditions of the said Agreement or to extend time of performance by the said contractor(s) from time to time or from time to time any of the power exercisable by the Government against the said Contractor(s) and to forbear or enforce of the terms and conditions relating to the said agreement and we shall not be relieved from our liability by reason of any such variation, or extension being granted to the said Contractor(s) or for any  forbearance, act or omission on the part of the Government or any indulgence by the Government to the said contractor(s) or by any such matter or thing whatsoever which under the law relating to sureties would, but for this provision, have effect or so relieving us.

- This guarantee will not be discharged due to the change in the constitution of the Bank or the Contractor(s)/supplier(s).

- We (name of the bank)_____________________lastly undertake not to revoke this guarantee during its currency except with the previous consent of the Government in writing.

Dated the________________day of__________________

For____________________________________________

(indicate the name of   bank)

Annexure-II

Certificate on non-participation of near relatives in the tender.

I, Sri__________________________________________________________

S/O________________________________________________________________

Village______________________________P.O.____________________________P.S._________________________________Dist.___________________________hereby certify that none of my relative(s) defined below is/are employed in BSNL unit. In case at any stage, it is found that the information given by me is false/incorrect, BSNL shall have the absolute right to lake any action as deemed fit, without any prior intimation to me.

Signature of bidder_________________________

Date.

Definition of near relatives.

No sub-contracting is permissible by BSNL. The near relatives of all BSNL employees (Non-executive employees) working in telecom District, Bolangir  & executive employees (also called Group-A & Group-B officers) working in Orissa Telecom Circle either directly recruited or on deputation are prohibited from participation in this tender. The near relatives for this purpose are defined as :

- Members of a Hindu Undivided Family.

- They are husband and wife

- The one is related to the other in the member as father, mother son(s), son’s wife (daughter-in-law). Daughter(s) & daughter’s husband (son-in-law), brother(s) & brother’s wife, sister(s) sister’s husband (brother-in-law), relative is working in the units of BSNL as defined above. In case of proprietorship firm the certificate will be given by the proprietor, for partnership firm certificate will be given by all the partners and in case of limited company by all Directors of the Company. Any breach of these conditions by the company or firm or any other person, the tender/work will be cancelled and earnest money/security deposit will be forfeited at any stage whenever it is noticed. The BSNL will not pay any damages to the company or firm or concerned person. The company or firm or the person will also be debarred from further participation in the concerned unit.

##### ANNEXURE-III

### FINANCIAL BID

Details of Item and quantity of work for making earthlings at 25 sites in

Bolangir  SSA

| Sl.No. | Schedule of work | Unit | Rate in figures | Rate in Words |
| --- | --- | --- | --- | --- |
| 1 | Digging of earth pit 10’ X 10’ X 15’ and boring at the center of the earth pit for about 10 ft or more depending on the nature of soil, if required to introduce the copper strip to obtain the ohmic value of the earth less than 0.5 ohms | Per pit |  |  |
| 2 | Supplying soft soil for filling the earth pit | Per Pit |  |  |
| 3 | Supplying Charcoal for the earth pit | Per Bag |  |  |
| 4 | Charges for filling up the earth pit with soft soil, char coal and mixture in layer by layer of one foot thickness upto the ground level as per the diagram and also instructions of JTO/SDO/TTA concerned | Per Pit |  |  |
| 5 | Supplying and fixing of copper plate of size 2’X2’X4 mm in the earth pit including making holes fitting of nuts & bolts etc. and gas welding of the Copper strip with the copper plate and complete settings. | Per Plate |  |  |
| 6 | Supplying and providing G.I. pipe of medium gauge of size 15’ length of 50 mm. Dia | Per pipe |  |  |
| 7 | Supplying and making connections with two Copper strip from two diagonally opposite copper plate upto the earth bus-bar and making terminations with proper size of copper sockets including materials & lugging etc. | Per Mtr. |  |  |
| 8 | Removal of surplus earth from the site and spreading inside the compound as per direction of BSNL official/officer | Per Site |  |  |

NOTE :

- The earth resistance should be 0.5 Ω or less at any cost otherwise payment will not be made till rectification.

- The rates to be quoted should be inclusive of all taxes & transportation charges.

Signature of the bidder

With full address

Contact Telephone No:

Mobile/FAX No:

# Text boxes

Telecom District Manager Bolangir

Vertical  View

Bus Bar Size =

10’x2’x6mm

50mm GI Pipe

0.5’

Good Quality loose soil (preferably black soil)

0.5’

Charcoal

Good Quality loose soil (preferably black soil)

0.5’

Charcoal

0.5’

0.5’

Good Quality loose soil (preferably black soil)

10’

10’

10’

1.5’

0.5’

Stripe Size =

50mm x 3mm

Plate Size =

2’x2’x4mm thick

Horizontal  View

Charcoal

Good Quality loose soil

(preferably black soil)