# AMENDMENT -I

## No:- D-286/OFC/MBTS/2009-10/7 	                Date: 26.05.2009

The following Amendment has been issued to

D-286/OFC/MBTS/2009-10/1   Date: 14.05.2009

- Page No. 38(Zone wise Detailed Quantum of work :-   Description of work of Sl. No-1.

SECTION – VIII

Zone wise Detailed Quantum of work

(Unit in Mtr)

| Sl. No. | Discription of Work | Unit in Mtr. | Name of Route. |
| --- | --- | --- | --- |
|  |  |  | Zone- I | Zone-II | Zone-III | Zone-IV | Zone-V | Zone VI | Zone VII | Zone VIII |
|  |  |  | MAIDHARPUR | TULSIPAL | MUNDIDEULI | BHUSAN | SURA PRATAPPUR | KANIHA BTS | KULUMA –I (Rengali Side) | KULUMA –II (Kuluma Side) | Paiksahi | Kangula | Banara | Bajrakote | Gadapalasuni | Dera –I (Dera Side) | Dera –I I (Ananta Side) |
| 1 | Excavation of trenches of 45 cms width the top and 30 cms width at the bottom to a depth of 165 cms, ramming of bottoms as required and then reinstating the soil in layers of 20cms including consolidating each deposited layer by ramming, watering etc and disposing of the surplus excavated soil as directed within a lead of 50cm. This includes jungle cutting, dewatering and removing obstacles, if any. | SOFT SOIL | 85 | 60 | 140 | 1450 | 3080 | 2690 | 1660 | 2075 | 760 | 45 | 48 | 35 | 115 | 875 | 875 |
|  |  | Rocky (Morrum) | 30 | 20 | 85 | 725 | 900 | 855 | 1245 | 1040 | 95 | 25 | 16 | 5 | 38 | 440 | 440 |
|  |  | HARD ROCK | 25 | 20 | 55 | 725 | 500 | 855 | 1245 | 1035 | 95 | 20 | 16 | -- | 37 | 435 | 435 |

- Date & time of sale of tender paper  is extended up to 16.00 hrs of  04.06.2009

- Date & time of submission of tender paper is extended up to 13.00 hrs of  05.06.2009

- Date & Time of opening of tender is extended up to 16.00 hrs. of  05.06.2009

- If any Tender is received by the U/S with old document, the bidder will be allowed to re-submit his financial bid which will be sealed in the presence of other bidders on the technical bid opening date.

- All other terms and conditions remains the same.

D.E.(P&A)

O/O G.M.T.D. Dhenkanal

# Text boxes

BHARAT  SANCHAR  NIGAM  LIMITED

(A Government of India Enterprise)

O/o the General Manager Telecom District,

Dhenkanal-759001